GF-MESM

Multi Engine Start Module

Congratulations on your purchase of a GoFlight GF-MESM (Multi Engine Start Module, part of the extensive

family of GoFlight GF-AC Cockpit Control System modules. The GF-MESM is designed to operate with a wide variety of

aircraft and is sure to make your flight simulation

experience more realistic and enjoyable.

The steps below will assist in the installation, configuration and operation of the GF-MESM. Following these instructions

will help to get you up in the “virtual skies” as quickly as possible.

Installing the GF-MESM

NOTE If you own other GoFlight hardware and have already installed the most current version of software on your system, you do not need to install the software again. Simply skip the software installation steps in the instructions below.

1. Get on line and go to www.goflightinc.com.

2. On the home page click Support tab then Latest Software Update

3. Click on Latest Software Up-date to download our latest module drivers and configuration

Software.

4. Click “Run” or “Save” and follow the instruction to load your software.

If the software installer detects that GoFlight software is already installed on your system, it

will prompt you to overwrite. Click the Yes button to overwrite the existing version of GoFlight software. This is useful if you wish to keep the configuration settings for other GoFlight modules installed on your system. However, you should first make sure that the software you are overwriting is an older version and not a newer one.

5. Plug the USB cable “B” connector end (square) into the connector on the back of the GF-MESM

circuit board.

6. Plug the USB cable “A” connector end (rectangular) to a USB port on your computer or USB hub. Once the operating system recognizes the GF-MESM, you will see the GF-MESM Picture on the left side of the program window. Each time you start GF-Config the picture indicates that the GF-MESM has been detected by your computer and is ready to use.

Installing the GF-MESM into the GoFlight Flight Deck Console

1. If you are planning to install the GF-MESM module into a GoFlight rack enclosure, install the module in any desired location in the enclosure. Fasten the module in place using the two thumbscrews that are included in the GF-MESM packaging being careful not to over-tighten them.

- After you install the GoFlight software and connected the GF-MESM for the first time, run the GF-Config program, which is located in your Programs menu under “GoFlight”. Verify that GF-Config displays a picture example representing the GF-MESM unit on the left-hand side of the program window. Click on the GF-MESM picture to show the configuration options in the right side of the program window.

Configuring the GF-MESM

To Setup your GF-MESM for the default aircraft.

In GF-Config use the cockpit function menu.

Example: Click on LStart knob turn CCW “Counter Clockwise” and set the cockpit function to

ENG_1_Starter_off.

Then click on LStart knob turn CW “Clockwise” and set the cockpit function to ENG_1_Starter_on

Repeat the process for the Right engine starter knob.

Note: There is no setting for the EGN Switch for the FS Default Aircraft.

The GF-MESM can also be used for add on aircraft using the Key Sequence feature.

To setup your GF MESM with add-on aircraft you will need to look at your add-on documentation to find the keystrokes that control the engine functions. Once you have found the keystrokes you will need to put them into GF-Config using the Key Sequence feature.

Open GF-Config and click on your MESM. Now to the right side of the program window choose the

Function to program. Then click on the Key Sequence and then Record. Now use your keyboard to set the keystroke for that function.

When you have finished selecting functions for your GF-MESM, exit GFConfig and run your Flight Sim

Program.

Note: The MESM also support’s FSUIPC for setting keystrokes.

If you have any questions or problems setting up your GF-MESM you can contact our Tech Support

At techsupport@goflightinc.com or call 503-895-7020

This product is warranted to the original purchaser to be free from defects in materials and workmanship for a period

of one (1) year from the date of purchase. During this warranty period, GoFlight Technologies, Inc. ® (“GoFlight”) will, at its option, repair or replace, at no charge, any component determined to be defective. The liability under this warranty is limited to the repair and/or replacement of the defect or defective part, and does not include shipping expenses. This warranty does not apply if, in the determination of GoFlight, this product has been damaged by accident, abuse, improper usage, or as a result of service or modification by anyone other than GoFlight.

NO OTHER WARRANTIES ARE EXPRESSED OR IMPLIED, INCLUDING BUT NOT LIMITED TO IMPLIED WARRANTIES OF SALABILITY AND FITNESS FOR A PARTICULAR PURPOSE. GOFLIGHT TECHNOLOGIES, INC. IS NOT RESPONSIBLE FOR CONSEQUENTIAL DAMAGES. SOME STATES DO NOT ALLOW EXCLUSION OR LIMITATION OF INCIDENTAL OR CONSEQUENTIAL DAMAGES, SO THE ABOVE LIMITATION OR EXCLUSION MAY NOT APPLY TO YOU.

This warranty gives you specific legal rights, and you may also have other rights which vary from state to state.

GoFlight Technologies, Inc. 163 SW Freeman Ave. Suite D, Hillsboro, Oregon, USA 97123

Phone: 1-503-895-0242

www.goflightinc.com

P/N GF-RP48-vPOH-002 Revision 2.2 25Nov2010

Copyright © 2010 GoFlight Technologies, Inc. All rights reserved.